The City of Guadalupe is working hard to produce the highest quality drinking water for our customers.

The City receives water from two sources: ground water wells and State Water (through membership with the Central Coast Water Authority.) Both sources are monitored and assessed in accordance with government standards and monitoring requirements. Checking quality and identifying potential problems was one of our goals.  We are proud to say that the water delivered to your home in 2011 complied with all State and Federal drinking water requirements.

The City prepares an annual report to inform customers of the quality of water being delivered. This report contains data from January 1st 2011 to December 31st 2011 testing results, and shows that the water delivered to your home, complied with regulated standards and is reliable for domestic use.

For more information about this report, or for questions about any topic related to water and water quality, please contact the Water Department Supervisor at (805) 356-3890.

ESPANOL: Este informe contiene información importante sobre su agua de beber y como cumple con los estándares estatales y federales. Tradúzcalo o hable con alguien que lo entienda bien. Si no encuentra la manera de entender este reporte, por favor contacte el departamento de agua de la ciudad de Guadalupe al  (805) 356-3890.

## City of Guadalupe Water System

The City of Guadalupe water system consists of two pumping stations, three storage tanks, and various water mains. Safe treatment and distribution of water is our daily goal.  Maintaining pumping stations, tanks and mains is vital to achieving that goal.  The City also has security measures in place to ensure that our water supply gets to our residents safely and efficiently.

City of Guadalupe 2011

#### WATER QUALITY

This report provides information regarding the quality of water for the City of Guadalupe during 2011. Included are details about where your water comes from, what it contains, and how it compares to drinking water standards.

918 Obispo Street-Guadalupe, CA 93434

(805) 356-3890

www.ci.guadalupe.ca.us

CITY OF GUADALUPE

WATER SOURCE DETECTIONS (FROM ACTIVE WATER WELLS)

| TABLE 1 – SAMPLING RESULTS ON DETECTION OF COLIFORM BACTERIA |
| --- |
| Microbial Contaminant | Highest No. of Detections in a month | No. of Months in Violation | MCL | PHG (MCLG | Major Sources of Bacteria |
| Total Coliform Bacteria | 1 | None | 5% of Monthly samples Positive. | 0 | Natural Present in the Environment |
| Fecal Coliform or E.coli | None | None | A routine sample and repeat sample detecting positive coliform, and either sample detects. | 0 | Human and animal fecal waste |
| TABLE 2- SAMPLING RESULTS ON DETECTION OF LEAD AND COPPER |
| Lead and Copper | Date | No. of Samples Collected | 90th Percentile level detected | No. of Sites Exceeding AL | AL | PHG (MCLG) | Typical Source of Contaminant |
| Lead (ppb) | 8/2011 | 20 | ND | 0 | 15 | 0.2 | Internal corrosion of household water plumbing systems; discharges from industrial manufacturers; erosion of natural deposits |
| Copper (ppb) | 8/2011 | 20 | 110 | 0 | 1300 | 170 | Internal corrosion of household plumbing systems; erosion of natural deposits; leaching from wood preservatives |
| TABLE 3 – SAMPLING RESULTS FOR SODIUM AND HARDNESS |
| Chemical or Constituent (and reporting units) | Sample Date | Average Level Detected | Range of Detections | MCL | PHG (MCLG) | Typical Source of Contaminant |
| Sodium (ppm) | 3/15/11 | 42 | 42 | None | None | Salt present in the water and is generally naturally occurring |
| Hardness (ppm) | 3/15/11 | 420 | 420 | None | None | Sum of polyvalent cations present in the water, generally magnesium and calcium, and are usually naturally occurring |
| TABLE 4 – DETECTION OF CONTAMINANTS WITH PRIMARY DRINKING WATER STANDARD |
| Chemical or constituent (and reporting units) | Sample Date | Average Level Detected | Range of Detections | MCL | PHG (MCLG) | Major Sources in Drinking Water |
| Total Trihalomethanes (ppb) | 12/1/11 | 15.6 | 15.6 | 80 | N/A | By-product of drinking water disinfection |
| Haloacetic Acids (ppb) | 12/1/11 | 8.3 | 8.3 | 60 | N/A | By-product of drinking water disinfection |
| Arsenic (ppb) | 3/15/11 | ND | ND | 10 | .004 | Erosion of natural deposits; runoff from orchards; glass and electronics production wastes |
| Fluoride (ppm) | 3/15/11 | 0.21 | 0.21 | 2 | 1 | Erosion of natural deposits; water additive that promotes strong teeth; discharge from fertilizer and aluminum factories |
| Nitrate as NO3 (ppm) | 1/11/11, 3/15/11 | 1.1 | ND – 2.1 | 45 | 45 | Runoff and leaching from fertilizer use; leaching from septic tanks and sewage; erosion from natural deposits |
| Nitrite as N (ppb) | 3/15/11 | 480 | 480 | 10000 | 10000 | Runoff and leaching from fertilizer use; leaching from septic tanks and sewage; erosion from natural deposits |
| Total Chlorine Residual (ppm) | Daily | 1.41 | 1.26 – 1.58 | MRDL = 4.0 | MRDLG = 4.0 | Drinking water disinfectant added for potable water treatment |
| Uranium (pCi/L) | 4/26/11 | 2.7 | 2.7 | 20 | 0.43 | Erosion of natural deposits |
| Gross Alpha (pCi/L) | 3/1/11, 8/2/11 | 4.5 – 5.9 | 5.2 | 15 | (0) | Erosion of natural deposits |
| TABLE 5 – DETECTION OF CONTAMINANTS WITH SECONDARY DRINKING WATER STANDARD |
| Chemical or constituent (and reporting units) | Sample Date | Average Level Detected | Range of Detections | MCL | PHG (MCLG) | Major Sources in Drinking Water |
| Chloride (ppm) | 3/15/11 | 19 | 19 | 500 | N/A | Runoff/leaching from natural deposits; seawater influence |
| Color (ACU) | 3/15/11 | ND | ND | 15 | N/A | Natural –occurring organic materials |
| Corrosivity (SI) | Non-Corrosive | Non Corrosive | Non-Corrosive | N/A | N/A | Natural or industrially-influenced balance of hydrogen, carbon and oxygen in the water; affected by temperature and other factors. |
| Iron (ppb) | 3/15/11 | ND | 170 – 230 | 300 | N/A | Leaching from natural deposits; industrial wastes |
| Manganese (ppb) | 3/15/11 | ND | 34 | 50 | N/A | Leaching from natural deposits |
| Odor Threshold (TON) | 3/15/11 | 1 | 1 | 3 | N/A | Naturally-occurring organic materials |
| Specific Conductance ((mho/cm) | 3/15/11 | 940 | 940 | 1600 | N/A | Substances that form ions when in water; seawater influence |
| Sulfate (ppm) | 3/15/11 | 280 | 280 | 500 | N/A | Runoff/leaching from natural deposits; industrial wastes |
| Total Dissolved Solids (ppm) | 3/15/11 | 640 | 640 | 1000 | N/A | Runoff/leaching from natural deposits |
| Turbidity (NTU) | 3/15/11 | ND | ND | 5 | N/A | Soil runoff |
| TABLE 6 – DETECTION OF UNREGULATED CONTAMINANTS |
| Chemical or constituent (and reporting units | Sample Date | Average Level Detected | Range of Detections | MCL | PHG (MCLG) | Major Sources in Drinking Water |
| Alkalinity (ppm) | 3/15/11 | 210 | 210 | N/A | N/A | Runoff/leaching from natural deposits; seawater influence |
| Bicarbonate (ppm) | 3/15/11 | 260 | 260 | N/A | N/A | -- |
| Calcium (ppm) | 3/15/11 | 120 | 120 | N/A | N/A | Runoff/leaching from natural deposits; seawater influence |
| MBAS (ppm) | 3/15/11 | ND | ND | 0.5 | N/A | Municipal and industrial waste discharges |
| Magnesium (ppm) | 3/15/11 | 40 | 40 | N/A | N/A | Runoff/leaching from natural deposits; seawater influence |
| pH (units) | 3/15/11 | 7.7 | 7.7 | N/A | N/A | Runoff/leaching from natural deposits; seawater influence |
| Potassium (ppm) | 3/15/11 | 2.3 | 2.3 | N/A | N/A | Runoff/leaching from natural deposits; seawater influence |
| TABLE 7 – DETECTION OF UNREGULATED CONTAMINANTS WITH NOTIFICATION LEVELS |
| Chemical or constituent (and reporting units | Sample Date | Average Level Detected | Range of Detections | NL | PHG (MCLG) | Possible Health Effects |
| Boron (ppb) | 3/15/11 | 130 | 130 | 1000 | N/A | Babies of some pregnant women who drink water, containing boron in excess of the notification level may have an increased risk of developmental effects, based on studies in laboratory animals. |
| Vanadium (ppb) | 3/15/11 | 6.2 | 6.2 | 50 | N/A | Babies of some pregnant women who drink water, containing boron in excess of the notification level may have an increased risk of developmental effects, based on studies in laboratory animals. |

# PURCHASED SURFACE WATER

CENTRAL COAST WATER AUTHORITY

|  |  |  | TREATED | SOURCE |  |
| --- | --- | --- | --- | --- | --- |
| Parameter | Units | State MCL | PHG (MCLG) | State DLR | Range Average | CCWA PPWTP | STATE WATER | Major Sources in Drinking Water |

PRIMARY STANDARDS—Mandatory Health-Related Standards

Clarity (a)

| Combined Filter Effluent Turbidity | NTU | TT=<1 NTU every 4 hours TT=95% of samples <0.3 NTU | Range | 0.04 – 0.09 | NA | Soil runoff |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  | % | 100% | NA |  |

INORGANIC CHEMICALS

| Aluminum | ppm | 1 (b) | 0.6 | 0.05 | Range | ND - 130 | ND - 300 | Residue from water Treatment process; Erosion of natural deposits |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | Average | 70 | 130 |  |
| Nitrate as Nitrogen | ppm | 10 | 10 | 0.4 | Range | 0.41 | 0.41 | Runoff and leaching from fertilizer use; leaching from septic tanks and sewage; erosion from natural deposits |
|  |  |  |  |  | Average | 0.41 | 0.41 |  |

DISTRIBUTION SYSTEM MONITORING

| Total Chlorine Residual | ppm | MRDL=4.0 | MRDLG=4.0 | -- | Range | 1.3 – 3.1 | NA | Measurement of the disinfectant used in the production of drinking water |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | Average | 2.2 | NA |  |
| Total Trihalomethanes (d) | ppb | 80 | NA | NA | Range | 19 - 67 | NA | By-product of drinking water chlorination |
|  |  |  |  |  | Average | 40 | NA |  |
| Haloacetic Acids (d) | ppb | 60 (e) | NA | NA | Range | 8.6 - 18 | NA | By-product of drinking water chlorination |
|  |  |  |  |  | Average | 14 | NA |  |

SECONDARY STANDARDS—Aesthetic Standards

| Chloride | ppm | 500 | NA | NA | Range | 17 - 78 | 16 - 74 | Runoff/leaching from natural deposits; seawater influence |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | Average | 38 | 35 |  |
| Color | ACU | 15 | NA | NA | Range | ND | 20 | Naturally-occurring organic materials |
|  |  |  |  |  | Average | ND | 20 |  |
| Iron, Total | ppm | 0.3 | NA | 0.1 | Range | ND | 0.24 | Balance of hydrogen, carbon, & oxygen in water, affected by temperature & other factors |
|  |  |  |  |  | Average | ND | 0.24 |  |
| Odor Threshold | Units | 3 | NA | 1 | Range | 1 | 1 – 10 | Naturally-occurring organic materials |
|  |  |  |  |  | Average | 1 | 2 |  |
| Specific Conductance | (S/cm | 1600 | NA | NA | Range | 208 – 467 | 166 - 410 | Substances that form ions when in water; seawater influence |
|  |  |  |  |  | Average | 311 | 274 |  |
| Sulfate | ppm | 500 | NA | 0.5 | Range | 38 | 23 | Runoff/leaching from natural deposits; industrial wastes |
|  |  |  |  |  | Average | 38 | 23 |  |
| Total Dissolved Solids | ppm | 1000 | NA | NA | Range | 123 – 277 | 98 - 242 | Runoff/leaching from natural deposits |
|  |  |  |  |  | Average | 190 | 166 |  |
| Turbidity (Monthly) | NTU | 5 | NA | NA | Range | 0.04 – 0.10 | 0.68 – 18 | Soil runoff |
|  |  |  |  |  | Average | 0.05 | 4.9 |  |

ADDITIONAL PARAMETERS (Unregulated)

| Alkalinity (Total) as CaCO3 equivalents | ppm | NA | NA | NA | Range | 34 – 70 | 36 – 74 | Runoff/leaching from natural deposits; seawater influence |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | Average | 50 | 54 |  |
| Calcium | ppm | NA | NA | NA | Range | 22 - 54 | 20 - 52 | Runoff/leaching from natural deposits; seawater influence |
|  |  |  |  |  | Average | 37 | 37 |  |
| Hardness (Total) as CaCO3 | ppm | NA | NA | NA | Range | 40 – 96 | 40 - 98 | Leaching from natural deposits |
|  |  |  |  |  | Average | 68 | 68 |  |
| Heterotrophic Plate Count (f) | CFU/mL | TT | NA | NA | Range | 0 - 2 | NA | Naturally present in the environment |
|  |  |  |  |  | Average | 0.4 | NA |  |
| Magnesium | ppm | NA | NA | NA | Range | 6.7 | 6.8 | Runoff/leaching from natural deposits; seawater influence |
|  |  |  |  |  | Average | 6.7 | 6.8 |  |
| pH | pH Units | NA | NA | NA | Range | 7.3 – 9.5 | 7.6 – 9.5 | Runoff/leaching from natural deposits; seawater influence |
|  |  |  |  |  | Average | 8.3 | 8.3 |  |
| Potassium | ppm | NA | NA | NA | Range | 1.8 | 1.9 | Runoff/leaching from natural deposits; seawater influence |
|  |  |  |  |  | Average | 1.8 | 1.8 |  |
| Sodium | ppm | NA | NA | NA | Range | 32 | 25 | Runoff/leaching from natural deposits; seawater influence |
|  |  |  |  |  | Average | 32 | 25 |  |
| Total Organic Carbon (TOC) (g) | ppm | TT | NA | 0.30 | Range | 1.3 – 2.4 | 2.1 – 4.4 | Various natural and manmade sources |
|  |  |  |  |  | Average | 1.8 | 3.2 |  |

Footnotes: Abbreviations

(a) Turbidity (NTU) is a measure of the cloudiness of the water and it is a good indicator of the effectiveness of our filtration system. Monthly turbidity values are listed in the Secondary Standards section.

(b) Aluminum has a Secondary MCL of 200 ppb.

(c) Total coliform MCLs: No more than 5.0% of the monthly samples may be Total Coliform positive. Fecal coliform/E. coli MCLs: The occurrence of 2 consecutive Total Coliform positive samples, one of which contains fecal coliform/E. coli, constitutes an acute MCL violation. These MCLs were not violated in 2010. Out of 548 samples collected in 2010, one positive Total Coliform was detected on January 19, 2010. All required follow-up and confirmation samples collected in response ot the positive Total Coliform detection were absent for Total Coliform.

(d) Compliance based on the running quarterly annual average of distribution system samples.

(e) Monochloroacetic Acid (MCAA) has a DLR of 2.0 ug/L while the other four Haloacetic Acids have DLR's of 1.0 ug/L.

(f) Pour plate technique -- monthly averages.

(g) TOCs are taken at the treatment plant's combined filter effluent. pCi/L = PicoCuries per liter

(h) State MCL is 45 mg/L as nitrate, which equals 10 mg/L as N. PHG = Public Health Goal

AL = Regulatory Action Level

ACU = Apparent Color Units

CCWA= Central Coast Water Authority

CFU/ml = Colony Forming Units per milliliter

DHS = Department of Health Services

DLR = Detection Level for purposes of Reporting

MCL = Maximum Contaminant Level

MCLG = Maximum Contaminant Level Goal

MFL = Million Fibers Per Liter

MRDL = Maximum

MRDLG = Maximum Residual Disinfectant Goal

NA = Not Applicable

NC = Not Collected

NL = Notification Level

NTU = Nephelometric Turbidity Units

pCi/L = PicoCuries per liter

PHG = Public Health Goal

ppb = parts per billion, or micrograms per liter (μg/L)

ppm = parts per million, or milligrams per liter (mg/L)

PPWTP = Polonio Pass Water Treatment Plant

SI = Saturation Index

TOC = Total Organic Carbon

TT = Treatment Technique

UCMR = Unregulated Contaminant Monitoring Regulation

μmho/cm = micromhos per centimeter (unit of specific conductance of water).

The sources of drinking water (both tap water and bottled water) include rivers, streams, ponds, reservoirs, springs, and wells. As water travels over the surface of the land or through the ground, it dissolves naturally occurring minerals and, in some cases, hazardous materials. It can also pick up substances resulting from the presence of animals or from human activity.

Contaminants that may be present in source water include:

(Microbial Contaminants, such as viruses and bacteria, that may come from sewage treatment plants, septic systems, agricultural livestock operations, and wildlife.

(Inorganic contaminants, such as salts and metals, that can be naturally-occurring or result from urban storm water runoff, industrial or domestic wastewater discharges, oil and gas production, mining, or farming.

(Pesticides and herbicides, which may come from a variety of sources such as agricultural and urban storm water runoff, and residential uses.

(Organic chemical contaminants, including synthetic and volatile organic chemicals, that are byproducts of industrial processes and petroleum production, and can also come from gas stations, urban storm water runoff, agricultural applications, and septic systems.

(Radioactive contaminants,  which can be naturally-occurring or be the results of oil and gas production and mining activities.

In order to ensure that tap water is safe to drink, USEPA and the State Department of Health Services, (CDPH) prescribe regulations that limit the amount of certain contaminants in water provided by public systems.  Department regulations also establish limits for contaminants in bottled water that must provide the same protection for public health.

In 2011, the City of Guadalupe received 19.45% of its water supply from State water project (CCWA-Central Coast Water Authority).  Surface water is treated conventionally at the Polonio Pass Water Treatment Plant. For details on treatment process from state water project, please call the City of Guadalupe Water Dept. Supervisor at (805) 356-3890.

(Maximum Contaminant Level (MCL): The highest level of a contaminant that is allowed in drinking water. Primary MCL’s are set as close to the public health goals as is economically and technologically feasible. Secondary MCL’s are set to protect the odor, taste and appearance of drinking water.

(Maximum Contaminant Level Goal (MCLG): The level of a contaminant in drinking water below, which there is no known or expected risk to health.  MCLG’s are set by the U.S. Environmental Protection Agency (USEPA).

(Public Health Goal (PHG):  The level of a contaminant in drinking water below, which there is no known or expected risk to health. PHG’s are set by the California Environmental Protection Agency.

(Maximum Residual Disinfectant Level (MRDL):  The highest level of a disinfectant allowed in drinking water. There is convincing evidence that addition of a disinfectant is necessary for control of microbial contaminants.

(Maximum Residual Disinfectant Level Goal (MRDLG): The level of a drinking water disinfectant below, which there is no known or expected risk of health.  MRDLG’s do not reflect the benefits of the use of disinfectants to control microbial contaminants.

(Primary Drinking Water Standards (PDWS): MCL’s or MRDL’s for contaminants that affect health along with their monitoring and reporting requirements, and water treatment requirements.

(Secondary Drinking Water Standards (SDWS): MCL’s for contaminants that affect taste, odor, or appearance of the drinking water. Contaminants with SDWS’s do not affect the health at the MCL levels.

(Treatment Technique (TT): A required process intended to reduce the level of a contaminant in drinking water.

(Regulatory Action Level (AL): The concentration of a contaminant that a water system must follow.

Drinking water, including bottled water, may reasonably be expected to contain at least small amounts of some contaminants. The presence of contaminants does not necessarily indicate that the water poses a health risk.  More information about contaminants and potential health effects can be obtained by calling the USEPA’s Safe Drinking Water Hotline at the number below.  Some people may be more vulnerable to contaminants in drinking water than the general population.  Immuno-compromised persons such as persons with cancer undergoing chemotherapy, persons who have undergone organ transplants, with HIV/AIDS, or other immune system disorders, some elderly, and infants can be particularly at risk from infections.  These people should seek advice about drinking water from their health care providers.  USEPA/ Centers for Disease Control (CDC) guidelines on appropriate means to lessen the risk of infection by Cryptosporidium and other microbial contaminants are available from the Safe Drinking Water Hotline at (1-800-426-4791) or www.epa.gov/safewater/resource.

An Assessment of the drinking water source(s) for the City of Guadalupe found that they were most vulnerable to the following activities associated with contaminants detected in the water supply:  Runoff and leaching from fertilizer use, and erosion of natural deposits.

Nitrates: Due to high concentrations of Nitrates found in the water from one of our sources in the last few years, including 2011, the City does not use this source and will only use that source as an emergency source only. Nitrates in drinking water at levels above 45 mg/L is a health risk for infants of less than six months of age, pregnant woman and those with specific enzyme deficiencies.  Such nitrate levels in drinking water can interfere with the capacity of the infant’s blood to carry oxygen, resulting in serious illness; symptoms include shortness of breath and blueness of the skin. Nitrate levels may rise quickly for short periods of time because of rainfall or agricultural activity.

Lead & Copper: During 2011, all lead samples were under the DLR and therefore were reported as ND, and eight samples were above the detectible limit for copper, but the overall results did not indicate treatment required. If you are concerned with elevated levels of lead or copper in your home, you may have your water tested by contacting the City of Guadalupe Water Department.

THM’s and HAA’5: The City has been monitoring these contaminants with direction of state regulatory agencies, and there was a detection of the contaminants in our water. Included in this report you will find results of our monitoring.  Trihalomethanes and Haloacetic Acids are disinfection byproducts.  They are produced when a disinfectant, like chlorine, is added to the water and organic matter is present.  Some people who drink water containing THM’s and HAA’5’s in excess of the MCL over many years may experience liver, kidney or central nervous problems, and may have an increased risk of cancer.

About Water Blending: The City combines well water with State surface water to offset any contaminants that may be present in the water, and to ensure that the water delivered to your home meets all State and Federal drinking water requirements.

For questions: Please call the City of Guadalupe Water Department at (805) 356-3890.

Public Participation Opportunities: The Guadalupe City Council meets every 2nd and 4th Tuesday of the month at the Council Chambers located at 918 Obispo St. Guadalupe, CA.

# Text boxes

Detection of Contaminants Summary

City of Guadalupe Water Assessment

Additional Information on Drinking Water

## Definitions

WATER QUALITY

In Guadalupe

WATER QUALITY

# IN GUADALUPE